## Slide 1: Test1: Tabular Model
An Xgboost trained model.
This testcase is about multiple features (several 10’s of parameters)
  Attached csv file will have the full features.
Included script can be run easily to test the model.
  (Expected results are in the python script).
  Goal: Check if the parameters are tracked properly during training and validation.

## Slide 2: Test2: CNN Model
The models presented will be scratch wafer detection, binary classification CNNs.
  There are three different models: M1, M2, M3 with different sizes but roughly same accuracy and execution time.
  Goal: Measure if this sized model can be put easily and how fast it runs. Accuracy isn’t important since we already know that.
WM-811K (public dataset) was used to train these models. Some notes about this dataset:
  Total ~ 811,000 wafer images.
  172,950 wafers are labeled,
  25,519 wafers have real failure patterns
  147,431 wafers were still labeled none.
  Only ~ 1,200 wafers have the scratch defect pattern.
    800 used for training, rest 400 for validation and testing.
    This is a public dataset, so we don’t have any problems in divulging. Ref: https://www.kaggle.com/datasets/qingyi/wm811k-wafer-map

## Slide 3: Test2: Model Statistics
Model | Size | Precision | Recall | Accuracy | F1 Score | Input Dimension | Avg Prediction Time (per wafer)
Initial Model (M1) | 102 MB | 0.7273 | 0.7395 | 0.9963 | 0.7333 | 256x256 | 0.036559 sec
New Model (M2) | 74 MB | 0.8302 | 0.7395 | 0.9972 | 0.7822 | 128x128 | 0.036854 sec
Big Model (M3) | 328 MB | 0.1435 | 0.7815 | 0.9664 | 0.2424 | 256x256 | 0.039110 sec